## Slide 2: OCR-AMR System : WiFi-Based
WiFi
LTE/ethernet Router
OCR
Sensors
OCR
Sensors
OCR
Sensors
OCR
Sensors
Internet
Image Server
OCR
System/
Data Extraction
Data
Collection
Server

## Slide 3: OCR-AMR System : LoRa-based
WiFi
LTE/ethernet Router
OCR
Sensors
OCR
Sensors
OCR
Sensors
OCR
Sensors
Internet
Image Server
OCR
System/
Data Extraction
Data
Collection
Server
LoRa
Gateway

## Slide 4: Proposed OCR-based AMR Hardware System
ESP32
WiFi/BLE
Module
ESP32
Cam
Module
Power Module
(Battery, Voltage Regulators, chargers)
Voltage/Power Level
Indicators
(LEDs)
SDCard Reader

## Slide 5: Fast Prototyping for Image Acquisition System (v0.0)
ESP32
WiFi/BLE
Module
ESP32
Cam
Module
Power Module
(Battery, Voltage Regulators, chargers)
Voltage/Power Level
Indicators
(LEDs)

## Slide 6: Custom Circuit and Printed Circuit Board Design and Prototyping (v0.1)
ESP32
WiFi/BLE
Module
ESP32
Cam
Module
Power Module
(Battery, Voltage Regulators, chargers)
Voltage/Power Level
Indicators
(LEDs)
Custom PCB

## Slide 7: Hardware Phases
Phase 1 : Fast Prototyping
  Off-the-shelf components
Phase 2 : Custom Circuit/PCB Prototype
  Custom circuit/PCB Design
  Initial PCB Fabrication Turn-Around
Phase 3 : Improvements/Modifications
  Towards product finalization
  Packaging constraints

## Slide 8: Initial Test Setup for Image Acquisition
Test Meter
OCR-AMR
Adjustable Mount
Image Route Options for Initial Data Gathering:
Google Drive ** (tested, working setup)
Remote (Internet Path) Server
9 cm

## Slide 9: Proposed Test Submeters for Image Collection:

## Slide 10: Initial Camera mount data
Sample Meralco KWH-meter : 16 cm diameter
From Initial Setup : Camera mount is around 24cm
We need short focal length with wide angle lens ( > 120 deg ) camera
Work around for testing:
  Test available some wide angle lens for smartphones

## Slide 11: Some Ideas
OCR
Sensors
Takes x images and store it.
Options: remote initiated, or time-based
Transmits images for storage in a collection server.
Options : remotely initiated, or time-based
Issues:
Time stamping – do we add real time clocks (RTC) to OCR-AMR devices
or time stamps are done in collection servers?